## Slide 1
SN BOSE SUMMER INTERNSHIP 2026 · NIT SILCHAR
Kernel-Based Fault Classification
in Analog Circuits
A physics-grounded machine learning pipeline for diagnosing Normal, Drift, Open, Short and
Noise faults across four analog circuit topologies — from LTspice simulation to a live web app.
Presented by Karan Kaushik | B.Tech ECE, NIT Silchar
Guided by Dr. Anish Kumar Saha
~60 min presentation

## Slide 2
ROADMAP
What We'll Cover — In Nine Parts
1. Motivation & Problem
Why analog fault diagnosis matters, and why it's hard
2. Circuits & Fault Theory
The physics behind 4 topologies and 5 fault types
3. Data Pipeline
LTspice sweeps that generate real, physics-based training data
4. Feature Engineering
The formulas turning waveforms into 17 numbers
5. Machine Learning
SVM theory, kernels, GridSearchCV, cross-validation
6. The Smart Fixes
Two engineering decisions that pushed accuracy higher
7. Results & Deep Analysis
78.43% accuracy — and exactly where and why it fails
8. Key Finding & Limits
A hard lesson about trusting your own accuracy numbers
9. Demo & Conclusion
The live app, what's next, and a wrap-up
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
01

## Slide 3
1. MOTIVATION
Why Fault Classification Matters
Analog circuits are everywhere
Filters, power supplies, sensor front-ends and communication links all rely on analog stages that quietly degrade before they fail outright.
Manual diagnosis doesn't scale
Reading an oscilloscope trace to guess whether a fault is drift, noise, or a bad connection takes an expert and doesn't scale to thousands of boards.
Faults are often silent
A drifting resistor or a noisy stage can still “work” while quietly producing wrong answers downstream.
The goal
Give a machine the output waveform and let it instantly say what's wrong — and which component is likely responsible.
PHOTO / SCHEMATIC
e.g. lab PCB, oscilloscope capture, or
simulation workstation photo
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
02

## Slide 4
1. MOTIVATION
The Real-World Cost of an Undiagnosed Fault
Component drift and disconnects rarely announce themselves. A few examples of what's at stake:
Medical devices
A drifting filter stage in a patient monitor can quietly shift a threshold reading long before an alarm ever fires.
Communication links
A degraded low-pass filter changes a receiver's bandwidth, raising bit-error rates without any visible failure.
Power electronics
A drifting or shorted component in a regulator stage can shorten the life of every downstream part it feeds.
Automotive sensors
Analog sensor front-ends drift with temperature and age; catching this early prevents cascading failures.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
03

## Slide 5
1. MOTIVATION
Why This Problem Is Genuinely Hard
Faults are continuous, not binary
Drift isn't a switch — a resistor slides gradually from healthy to faulty, so “normal” and “drift” can look nearly identical near the boundary.
Signatures overlap across circuits
An “open” fault looks similar (flat, non-charging output) whether it happens in an RC filter or an RLC network — the model must tell topology and fault apart together.
20 classes from limited data
4 circuits × 5 faults = 20 classes to separate from just ~1,019 simulated samples — roughly 50 examples per class.
Simulation vs. reality gap
LTspice gives clean, repeatable waveforms; real hardware adds temperature drift, tolerances and parasitic effects simulation can't fully capture.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
04

## Slide 6
1. MOTIVATION
Where This Fits in the Literature
Analog fault diagnosis has a real research history — this project sits inside an established, active line of work rather than starting from a blank page.
Classical: fault dictionaries & sensitivity analysis
Simulate the circuit under every hypothesized fault ahead of time, build a "dictionary" of expected responses, then match a real measurement against it. Accurate for the exact circuit modeled, but must be rebuilt from scratch for every new topology.
A standard split this project mirrors: soft vs. hard faults
The literature separates gradual, within/beyond-tolerance parameter drift ("soft faults") from catastrophic opens and shorts ("hard faults"). This project's five categories — Normal, Drift, Open, Short, Noise — map directly onto that same split.
Machine-learning classifiers are now the mainstream approach
Recent published work applies SVMs, k-NN, ensemble methods and CNNs to extracted or raw-waveform features for analog soft-fault diagnosis, with SVM-based studies frequently reporting 95%+ accuracy — but almost always on a single circuit at a time.
What differs here: most studies tune a classifier for one circuit. This project trains one SVM across four topologies at once, uses only physics-based (non-augmented) data, and adds a topology-aware correction step — part of why 78.43% sits below single-circuit literature numbers, on a harder, multi-topology problem.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
05

## Slide 7
PROBLEM STATEMENT & OBJECTIVE
One Waveform In. One Diagnosis Out.
Given the transient output voltage of an unknown analog circuit, automatically identify which circuit topology it is and which of five fault conditions it is currently experiencing — a 20-class classification problem solved end-to-end with physics-based simulation and a tuned SVM.
4
Circuit Topologies
RC · RLC · Sallen-Key · RC Ladder
5
Fault Types
Normal, Drift, Open, Short, Noise
20
Total Classes
4 circuits × 5 fault conditions
1019
Real Samples
From physics-based LTspice sweeps
What's novel here: the training data comes entirely from real LTspice physics (no synthetic augmentation), and a topology-aware correction rule catches physically impossible predictions — two choices that trade a higher but hollow accuracy for a lower, trustworthy one.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
06

## Slide 8
2. CIRCUITS & FAULT THEORY
Five Ways an Analog Circuit Can Misbehave
Normal
Component values sit at their nominal, healthy design point.
Drift
A component value slowly shifts from nominal — aging, temperature, wear.
Open
A component disconnects entirely — an infinite-resistance break in the path.
Short
A component is bypassed — a near-zero-resistance path forms across it.
Noise
Random disturbance is superimposed on an otherwise healthy signal.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
07

## Slide 9
2. CIRCUITS & FAULT THEORY
Fault Deep Dive: Drift
Drift models a component value that has gradually moved away from its design value — the most physically realistic and hardest-to-catch fault, since aging and temperature affect every real component.
R(t) = R0 · (1 + delta)
delta = fractional deviation from nominal
In this project, drift is generated by sweeping the same component (R or L) across a wide but realistic range with LTspice's .step param directive — not a single fixed shift, but a whole family of plausible drifted values.
Why it's the hardest fault
Unlike open/short (extreme, obvious limits), drift sits on a continuum right next to “normal.” Later in Results, drift turns out to be the single hardest fault type to classify across every circuit in this project.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
08

## Slide 10
2. CIRCUITS & FAULT THEORY
Fault Deep Dive: Open & Short
Open: resistance to infinity
R_open -> infinity (no current path)
This project's RC circuit models “open” by sweeping the resistor from 1 megaohm to 1 gigaohm with .step param — effectively blocking the charging path so Vout never rises.
Short: impedance to zero
Z_short -> 0 (component bypassed)
The RC circuit's “short” is modeled by sweeping the capacitor down to 0.1-10 picofarads (R fixed at 1 kilohm) — the RC time constant collapses to picoseconds, so Vout jumps to 5V almost instantly, just as a true short would.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
09

## Slide 11
2. CIRCUITS & FAULT THEORY
Fault Deep Dive: Noise
Noise doesn't come from a component value changing at all — it's additive random disturbance superimposed on an otherwise healthy waveform, modeled with a fixed signal-to-noise ratio.
v_noisy(t) = v_normal(t) + N(0, sigma^2)
sigma^2 = mean(v_normal^2) / 10^(SNR_dB / 10)
SNR = 25 dB | seed = 42 (reproducible)
In code: each circuit's own NORMAL waveforms are reused as the clean base signal, then Gaussian noise scaled to a 25 dB SNR is added with NumPy's seeded random generator — one noisy sample generated per normal sample, so class counts stay balanced.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
10

## Slide 12
2. CIRCUITS & FAULT THEORY
Four Circuit Topologies Under Test
SCHEMATIC
RC Low-Pass Filter
One resistor, one capacitor — the simplest baseline. A single-pole exponential charge/discharge response.
SCHEMATIC
RLC Series Circuit
Adds an inductor for an underdamped, oscillatory step response — richer dynamics than RC alone.
SCHEMATIC
Sallen-Key Active Filter
An op-amp based 2nd-order filter — the kind actually used in real analog signal-conditioning design.
SCHEMATIC
RC Ladder Network
Multiple RC stages cascaded together, producing a more complex multi-pole response.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
11

## Slide 13
2. CIRCUITS & FAULT THEORY
RC Low-Pass Filter — The Baseline
H(s) = 1 / (1 + sRC)
v(t) = V * (1 - e^(-t / RC))
tau = R * C (time constant)
R swept 100 ohm to 10 kilohm (normal/drift) with C fixed at 10 microfarad — tau ranges from about 1 ms to 100 ms.
Open: R swept 1 megaohm to 1 gigaohm — the charging path is effectively blocked, so Vout never rises.
Short: C swept down to 0.1-10 picofarad — tau collapses to picoseconds, so Vout jumps to 5V almost instantly.
SCHEMATIC + WAVEFORM
e.g. LTspice schematic and
step response screenshot
IN PLAIN TERMS (for the CSE side): Just a resistor and capacitor charging up, like a bucket filling with water — tau is simply how long that fill takes.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
12

## Slide 14
2. CIRCUITS & FAULT THEORY
RLC Series Circuit — Adding Oscillation
H(s) = 1 / (LCs^2 + RCs + 1)
omega_0 = 1 / sqrt(LC) zeta = (R/2) * sqrt(C/L)
L swept 1 mH to 100 mH (normal/drift), with R = 10 ohm and C = 100 microfarad fixed — a genuinely underdamped, oscillatory step response.
Because zeta is small, the output rings before settling — a signature no RC-only circuit can produce.
Open: R swept 1 megaohm to 1 gigaohm in series, blocking the current path entirely.
SCHEMATIC + WAVEFORM
e.g. LTspice schematic and
step response screenshot
IN PLAIN TERMS (for the CSE side): The inductor makes this circuit "overshoot and wobble" before settling, like a swing that bounces past its resting point a few times — that wobble is the key signal the model learns to spot.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
13

## Slide 15
2. CIRCUITS & FAULT THEORY
Sallen-Key Active Filter — A Real Design Pattern
f_c = 1 / (2*pi*sqrt(R1*R2*C1*C2))
Unity-gain, 2nd-order low-pass (op-amp based)
R1 = R2 swept 1 kilohm to 100 kilohm together; C1 = C2 = 10 nanofarad fixed; dual +-15V supply, LT1001 op-amp model.
This is the one topology here that's actually used in production analog signal-conditioning circuits — not just a textbook passive network.
Its op-amp feedback path gives it a distinct response shape from the three purely passive circuits.
SCHEMATIC + WAVEFORM
e.g. LTspice schematic and
step response screenshot
IN PLAIN TERMS (for the CSE side): An op-amp is just a powered amplifier chip with feedback wired around it — think of it as an "active" filter that can shape a signal more precisely than a passive RC network alone.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
14

## Slide 16
2. CIRCUITS & FAULT THEORY
RC Ladder Network — Cascaded Stages
Stage 1: 1/(1+sR1C1) -> Stage 2: 1/(1+sR2C2)
H(s) = Stage1(s) * Stage2(s) (multi-pole)
Two RC stages in series, R1 = R2 swept together 100 ohm to 10 kilohm, C1 = C2 = 10 microfarad — each stage contributes its own pole.
A fault in an earlier stage propagates and interacts with the second stage, producing subtler waveform changes than a single RC stage would.
This structural similarity to the plain RC circuit is exactly what makes the two easy to confuse later, in Results.
SCHEMATIC + WAVEFORM
e.g. LTspice schematic and
step response screenshot
IN PLAIN TERMS (for the CSE side): Two RC "buckets" chained together, one feeding into the next — more stages give a smoother, more gradual response than a single RC stage.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
15

## Slide 17
2. CIRCUITS & FAULT THEORY
Same Circuit, Five Different Personalities
Example: an RC low-pass filter's step response under each of the five fault conditions.
WAVEFORM
Normal response
Normal
WAVEFORM
Drift response
Drift
WAVEFORM
Open response
Open
WAVEFORM
Short response
Short
WAVEFORM
Noise response
Noise
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
16

## Slide 18
3. DATA PIPELINE
The End-to-End Pipeline
1
Simulate
Model 4 circuits in
LTspice XVII
2
Sweep
Vary R/L/C values
across realistic ranges
3
Extract
17 features per
waveform
4
Train & Tune
SVM kernels +
GridSearchCV
5
Correct
Topology-aware
post-processing
6
Deploy
Live Streamlit
web app
Every stage is grounded in real simulation physics — no synthetic data augmentation was used in the final pipeline, only genuine LTspice parameter sweeps.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
17

## Slide 19
3. DATA PIPELINE · STEP 1
Simulating Real Circuit Behavior in LTspice
Why SPICE instead of pure math?
LTspice's transient solver captures op-amp behavior, component tolerances and transient effects that a hand-derived transfer function alone would miss.
A step input drives every circuit
A PULSE voltage source jumps 0V to 5V (1ns rise time), mimicking a sudden real-world input change.
.tran captures the transient response
The .tran directive runs the simulation and records Vout at 200 time points as the circuit reacts to the step.
LTSPICE SCHEMATIC
e.g. screenshot of the .asc
circuit diagram in LTspice XVII
V1 PULSE(0 5 0 1n 1n 95m 200m)
.tran 95m
.step param Rval 100 10000 200
IN PLAIN TERMS (for the CSE side): Think of this like a unit test: give the circuit a sudden voltage change and record how it reacts over time — that recorded reaction is the raw data.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
18

## Slide 20
3. DATA PIPELINE · STEP 2
Parameter Sweeps: Simulating Real-World Variation
A single fixed waveform per fault would teach the model almost nothing. The .step param directive instead sweeps a component value across a realistic range, generating roughly 51 independent transient runs per fault class, per circuit.
Circuit
Normal / Drift sweep
Fixed components
RC
R: 100 ohm -> 10 kilohm
C = 10 uF
RLC
L: 1 mH -> 100 mH
R = 10 ohm, C = 100 uF
Sallen-Key
R1=R2: 1 kilohm -> 100 kilohm
C1=C2 = 10 nF, +-15V supply
RC Ladder
R1=R2: 100 ohm -> 10 kilohm
C1=C2 = 10 uF
~51 sweep steps x 4 circuits x 5 faults =~ 1,019 total samples
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
19

## Slide 21
3. DATA PIPELINE · STEP 2
How Each Fault Is Modeled in LTspice
Fault
Modeling mechanism
Concretely (RC example)
Normal
Component at nominal design value, swept across a healthy range
R: 100 ohm -> 10 kilohm
Drift
Same component, same wide sweep — treated as the healthy range itself
R: 100 ohm -> 10 kilohm
Open
Affected resistor swept toward near-infinite resistance
R: 1 megaohm -> 1 gigaohm
Short
Affected reactive component swept toward its opposite extreme
C: 0.1 pF -> 10 pF
Noise
Gaussian noise added post-hoc to normal waveforms, not simulated in LTspice
SNR = 25 dB, seed = 42
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
20

## Slide 22
3. DATA PIPELINE · STEP 2
From LTspice Output to a Clean Dataset
Each .step sweep produces one exported text file containing dozens of stacked runs. A parser walks the file, splits it back into individual runs, and resamples every run onto a common 200-point time grid:
for line in file:
if line starts with "Step Information": start new run
else: accumulate (time, voltage) pairs
resample(t, v, t_end, n=200):
grid = linspace(0, t_end, 200)
return interp1d(t, v)(grid) # uniform length for every sample
This turns dozens of variable-length LTspice runs into one uniform, ML-ready table of 200 voltage points per sample.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
21

## Slide 23
3. DATA PIPELINE · STEP 3
A Look at the Raw Dataset: master_dataset_sweep.csv
Every LTspice sweep run becomes one row: a circuit label, a fault label, the swept parameter value, and 200 raw voltage samples (v0 ... v199) tracing the full transient response. This is the direct, unprocessed output of Step 2 — nothing has been engineered yet.
id
circuit
fault
param_value
v0
v1
v2
...
v199
0
RC
normal
100 ohm
0.000
1.962
3.080
...
5.000
102
RC
open
n/a
0.000
0.000
0.000
...
0.047
153
RC
short
n/a
0.000
5.000
5.000
...
5.000
255
RLC
drift
12.0 mH
0.000
0.000
0.002
...
8.668
1,019 rows x 204 columns total. Notice how the shape alone tells a story: RC_open barely rises off 0V, RC_short jumps straight to 5V, and RLC_drift overshoots past 5V before settling — that oscillation ("ringing") is only possible because the RLC circuit has an inductor. A few param_value entries show as n/a because of a parsing quirk in the original sweep export — a real, minor rough edge left visible here rather than smoothed over.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
22

## Slide 24
3. DATA PIPELINE
1,019 Samples, Evenly Balanced Across Fault Types
Chart: 
| Normal | Drift | Open | Short | Noise
Samples | 204 | 204 | 204 | 203 | 204
Perfectly balanced classes
Each fault type accounts for about 20% of samples, so the model can't win by just guessing the majority label.
20 total labels
Each sample is tagged circuit_fault, e.g. RC_open or SALLEN_KEY_drift — 4 circuits times 5 faults.
About 51 samples per class
1,019 divided across 20 classes averages to roughly 51 samples each — a genuinely small-data problem.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
23

## Slide 25
3. DATA PIPELINE
Train/Test Split: Keeping Evaluation Honest
train_test_split(X, y, test_size=0.20, random_state=42, stratify=y)
80/20 split: About 815 samples train the model; the remaining ~204 are held out purely for evaluation.
Stratified by class: Every one of the 20 classes keeps its ~80/20 proportion in both sets — no class is accidentally left thin in testing.
Fixed random seed: random_state=42 makes the split reproducible — the same test samples every time the pipeline reruns.
Test set never touched during tuning: GridSearchCV only ever sees the training set; the test set is reserved for the one final, honest accuracy number.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
24

## Slide 26
4. FEATURE ENGINEERING
From Waveform to Numbers
Each raw sample is 200 individual voltage readings — too high-dimensional and noisy for a classic SVM to learn from efficiently. Instead, every waveform is compressed into 17 compact, physically meaningful numbers that fall into two families:
Time-domain shape
How the signal looks over time — peak voltage, RMS, rise time, settling time, skewness, kurtosis, DC level.
Frequency-domain content
How much energy sits at which frequency — dominant frequency, spectral energy, centroid, bandwidth, entropy.
ANNOTATED WAVEFORM
e.g. a single trace with peak voltage, rise time and settling time marked
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
25

## Slide 27
4. FEATURE ENGINEERING
Time-Domain Features: Amplitude & Shape
f1 peak_voltage = max(v)
f2 rms_value = sqrt( mean(v^2) )
f3 mean_voltage = mean(v)
f4 std_voltage = std(v)
These four numbers describe the basic size and spread of a waveform. A shorted capacitor pushes peak_voltage toward the full 5V almost immediately; an open circuit keeps it near 0V. std_voltage in particular turns out to be one of the two most important features in the trained model (see Results).
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
26

## Slide 28
4. FEATURE ENGINEERING
Time-Domain Features: Timing
f5 rise_time = t(at 90% peak) - t(at 10% peak)
f6 settling_time = last t where |v(t) - v_final| > 2% * |v_final|
rise_time is the single most important feature in the trained model — it directly captures how fast a circuit charges, which is exactly what open (never charges) and short (charges instantly) faults change most. settling_time captures how long oscillation or transients persist before the signal stabilizes.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
27

## Slide 29
4. FEATURE ENGINEERING
Time-Domain Features: Statistical Shape
f7 skewness = E[ (v - mean)^3 ] / std^3 (asymmetry)
f8 kurtosis = E[ (v - mean)^4 ] / std^4 (peakedness)
Borrowed from statistics, these describe the shape of the voltage distribution across the whole waveform, not just its size. A lopsided charge/discharge curve skews one way; a noisy signal has different kurtosis than a smooth one — useful signal the size-based features alone miss.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
28

## Slide 30
4. FEATURE ENGINEERING
Frequency-Domain Features: The FFT
The Fast Fourier Transform rewrites a signal from “voltage over time” into “energy at each frequency.” A smooth RC charging curve is dominated by low frequencies; noise spreads energy across many frequencies; an RLC's ringing shows a clear peak at its oscillation frequency.
V(f) = FFT( v(t) ) | magnitude spectrum |V(f)|
Five features (next slide) are computed from this magnitude spectrum rather than from the raw time signal.
IN PLAIN TERMS (for the ECE side): FFT is standard signal-processing math you already know from courses — this step is no different than reading a spectrum analyzer, just done in code instead of on a bench instrument.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
29

## Slide 31
4. FEATURE ENGINEERING
Frequency-Domain Features: Spectral Descriptors
f9 dominant_freq = f at max |V(f)|, 50-2000 Hz band
f10 spectral_energy = sum( |V(f)|^2 )
f11 spectral_centroid = sum(f*|V(f)|) / sum(|V(f)|) ("center of mass")
f12 bandwidth = sqrt( sum((f-centroid)^2 * |V(f)|) / sum(|V(f)|) )
f13 spectral_entropy = -sum( p(f) * log2 p(f) ), p(f)=|V(f)|^2/total
spectral_entropy is the third most important feature overall — a clean charging curve has low entropy (energy concentrated at low frequency); noise has high entropy (energy spread everywhere). This single number does a lot of work separating noise faults from everything else.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
30

## Slide 32
4. FEATURE ENGINEERING
Structural Features
f15 zero_crossing_rate = crossings of (v - mean(v)) per sample
f16 crest_factor = max(|v|) / rms_value
f14 energy = sum(v^2)
crest_factor is the fourth most important feature — it compares a signal's peak to its average power, which distinguishes a sharp, spiky waveform from a smooth one. zero_crossing_rate and energy add further structural context that complements the pure amplitude features.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
31

## Slide 33
4. FEATURE ENGINEERING
17 Features, Three Families
Time-Domain (9)
Peak voltage
RMS value
Mean voltage
Std. deviation
Rise time
Settling time
Skewness
Kurtosis
DC level
Frequency-Domain (5)
Dominant frequency
Spectral energy
Spectral centroid
Bandwidth
Spectral entropy
Structural (3)
Zero-crossing rate
Crest factor
Signal energy
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
32

## Slide 34
4. FEATURE ENGINEERING
Why Feature Scaling Matters
The 17 features live on wildly different scales — spectral_energy can be in the thousands while crest_factor is close to 1. An SVM's distance-based math would let large-scale features silently dominate, so every feature is standardized before training:
z = (x - mean) / std <- sklearn StandardScaler
Critically: the scaler is fit only on the training set, then applied to the test set — fitting on all the data first would leak test-set statistics into training and quietly inflate the reported accuracy.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
33

## Slide 35
4. FEATURE ENGINEERING
The Transformed Dataset: features_v2.csv
This is the file the SVM actually trains on. Each row still has one sample_id, circuit and fault label — but the 200 raw voltage points are now gone, replaced by the 17 engineered numbers (f1...f17) from the previous slides.
circuit
fault
f1 peak
f4 std
f5 rise_t
f9 dom.freq
f13 entropy
f17 dc_lvl
RC
open
0.047
0.014
0.076 s
52.4 Hz
0.926
0.045
RC
short
5.000
0.353
0.000 s
900.7 Hz
0.042
5.000
RLC
drift
8.668
2.835
0.062 s
52.4 Hz
1.243
8.276
SALLEN_KEY
noise
5.704
0.446
0.020 s
1194.0 Hz
0.063
5.064
1,019 rows x 20 columns (sample_id + circuit + fault + 17 features) — a 10x reduction from 204 columns, with each number chosen to carry physical meaning rather than just compressing data blindly. Notice RC_short and RLC_drift both have dominant_freq near 52 Hz while SALLEN_KEY_noise sits at 1194 Hz, and RC_short's spectral entropy (0.042) is far lower than RLC_drift's (1.243) — exactly the kind of separation the SVM will learn to exploit next.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
34

## Slide 36
5. MACHINE LEARNING
Support Vector Machines: The Big Idea
An SVM looks at labeled examples in feature space and draws the boundary that separates classes with the widest possible margin — not just any line that works, but the one furthest from the nearest points of each class.
Support vectors: Only the closest points to the boundary matter for defining it — these are the “support vectors” that give the algorithm its name.
Margin maximization: A wider margin between classes tends to generalize better to new, unseen data than a boundary that barely squeezes between them.
The kernel question: Real data is rarely separable with a straight line — the next slide covers how SVMs handle that.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
35

## Slide 37
5. MACHINE LEARNING
SVM Math: Hyperplanes & Margins
Decision boundary: w . x + b = 0
Classify: sign(w . x + b)
Margin width: 2 / ||w|| (maximize this)
Training objective: minimize ||w||^2 / 2, subject to correct classification
w is a weight vector (one number per feature) and b is a bias term. In the linear-kernel model, the size of each weight in w is literally what the Feature Importance chart (in Results) is built from — larger |weight| means that feature moves the boundary more.
IN PLAIN TERMS (for the ECE side): This is the same optimization idea as finding the best-fit line in a graph, just with a margin-width twist. You don't need to solve this by hand — scikit-learn's SVC does it in one line of code.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
36

## Slide 38
5. MACHINE LEARNING
The Kernel Trick
A straight-line boundary can't separate classes that curl around each other in feature space. Kernels let the SVM measure similarity as if the data had been projected into a higher-dimensional space — without ever computing that projection directly.
Kernel
Similarity function K(x, x')
Shape of boundary
Linear
x . x'
Straight line / flat plane
RBF
exp( -gamma * ||x - x'||^2 )
Smooth, flexible curve
Polynomial
(gamma * x . x' + r)^d
Curved, degree-d surface
gamma controls how far a single training example's influence reaches — this project's tuned RBF model uses gamma = 0.1.
IN PLAIN TERMS (for the ECE side): A "kernel" is just the shape of boundary the model is allowed to draw between classes — Linear is a straight cut, RBF and Polynomial can bend to fit curvier data.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
37

## Slide 39
5. MACHINE LEARNING
Multi-Class Strategy: One-vs-One
An SVM is naturally a binary (two-class) classifier. scikit-learn's SVC handles 20 classes by training one small binary classifier for every possible pair of classes, then combining their votes:
Number of binary classifiers = C(20, 2) = 20*19 / 2 = 190
decision_function_shape="ovo" (scikit-learn SVC default)
Each of the 190 mini-classifiers votes on which of its two classes a sample looks more like; the class with the most votes wins. This is what lets a single SVC model handle a 20-way problem without any special multi-class math of its own.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
38

## Slide 40
5. MACHINE LEARNING · STEP 1: BASELINE
Baseline Results — Before Any Tuning
Before touching a single hyperparameter, all three kernels are trained with scikit-learn's near-default settings (C=1.0, gamma="scale") on the same 80/20 split. This is the honest starting point every improvement from here on is measured against.
Linear
SVC(kernel="linear", C=1.0)
77.94%
test accuracy (default)
RBF
SVC(kernel="rbf", C=1.0, gamma="scale")
71.08%
test accuracy (default)
Polynomial
SVC(kernel="poly", C=1.0, gamma="scale", degree=3)
75.49%
test accuracy (default)
Even untuned, Linear already beats RBF — a sign the 17 hand-engineered features do real work before the classifier even sees them.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
39

## Slide 41
5. MACHINE LEARNING · STEP 2: TUNING
Tuning with GridSearchCV
The baseline numbers leave room on the table — untuned RBF scores only 71.1%. GridSearchCV exhaustively tries every combination in a grid of hyperparameters, scoring each with 5-fold cross-validation on the training set only.
Kernel
Grid searched
Combinations
Total fits (x5 folds)
Linear
C in {0.001 ... 1000} (7 values)
7
35
RBF
C (5) x gamma (6)
30
150
Polynomial
C (4) x gamma (3) x degree (2)
24
120
305 total model fits searched — best RBF found: C=100, gamma=0.1, lifting it from 71.1% to 76.96% before the topology rule.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
40

## Slide 42
5. MACHINE LEARNING · STEP 2: TUNING
Why 5-Fold Cross-Validation?
Testing one hyperparameter setting on a single train/validation split can just get lucky. 5-fold CV instead splits the training data into 5 equal chunks and rotates which chunk is held out:
Validate
Train
Train
Train
Train
Train
Validate
Train
Train
Train
Train
Train
Validate
Train
Train
Train
Train
Train
Validate
Train
Train
Train
Train
Train
Validate
Each of the 5 rows is one “fold”: 4/5 of the training data trains the model, 1/5 validates it — and the role rotates so every sample is validated on exactly once. The average across all 5 folds gives a far more reliable accuracy estimate than any single split.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
41

## Slide 43
5. MACHINE LEARNING · STEP 2: TUNING
Tuned Results — What GridSearchCV Bought Us
Linear
77.94% -> 77.45%
-0.49 pts vs. baseline
BEST MODEL
RBF
71.08% -> 78.43%
+7.35 pts vs. baseline
Polynomial
75.49% -> 77.94%
+2.45 pts vs. baseline
Note: the topology-aware correction rule (Section 6) is applied uniformly to all six numbers above, so these deltas isolate the effect of GridSearchCV tuning alone. Linear barely moves (and even dips slightly) because it was already close to its ceiling; RBF gains the most because its default gamma was poorly matched to the data.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
42

## Slide 44
6. THE SMART FIXES · PART 1
Diagnosing a Blind Spot: RC_open vs. RC_short
With the original 16 features, RC_open and RC_short were completely confused — F1 = 0.000. The fix came from a very direct diagnostic: compare the mean of each feature between the two classes and look for the biggest gap.
Feature
RC_open mean
RC_short mean
Separable?
peak_voltage
~0.02 V
~5.00 V
Yes — but noisy
rise_time
~0.095 s (never rises)
~0.000002 s (instant)
Marginal
dc_level (new)
~0.02 V
~5.00 V
Yes — cleanly
Both circuits settle to a flat line by the end of the observation window — the existing features just weren't capturing where that flat line actually sat.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
43

## Slide 45
6. THE SMART FIXES · PART 1
The Fix: A 17th Feature, dc_level
f17_dc_level = mean( v[-20:] ) # last 20 samples of the waveform
RC_open
Never charges within the 95ms window, so its steady-state DC level sits near 0V.
RC_short
Charges almost instantly with a collapsed time constant, so its steady-state DC level sits near 5V.
One new feature, directly targeting a diagnosed failure mode, fixed a class pair the other 16 features couldn't separate.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
44

## Slide 46
6. THE SMART FIXES · PART 2
Topology-Aware Post-Processing
A plain SVM can output a physically impossible label — e.g. "RLC_open" for a sample known to come from the RC circuit, which has no inductor to open at all. Rule: when the predicted class's circuit prefix doesn't match the sample's known true circuit, remap the fault type onto that circuit instead — e.g. RLC_open -> RC_open.
+1.47 points from this rule alone: 76.96% -> 78.43%
An honest limit: this rule only catches predictions that land on the wrong topology entirely. It can't fix a model that confidently predicts the wrong fault within the correct circuit — e.g. calling an RC_LADDER_short sample "RC_short" instead, since RC_short is a perfectly valid label, just for the wrong circuit's short fault. See the Confusion Matrix Deep Dive for exactly this case.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
45

## Slide 47
7. RESULTS & DEEP ANALYSIS
The Headline Number
78.43%
test accuracy on a 20-class problem, from real physics-based data alone
A random guess would score 5%. The next several slides break this single number apart: which kernel got us here, which circuits and faults it handles well, where it still struggles, and why the number itself is trustworthy.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
46

## Slide 48
7. RESULTS & DEEP ANALYSIS
RBF + Topology Rule Wins: 78.43%
Chart: Test Accuracy (%)
| Linear | RBF | Polynomial
Default | 77.94 | 71.08 | 75.49
Tuned + Topology Rule | 77.45 | 78.43 | 77.94
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
47

## Slide 49
7. RESULTS & DEEP ANALYSIS
Why These Kernel Results Make Sense
Why Linear already scores 77.9%
The 17 features are hand-engineered to be physically meaningful — rise_time, dc_level and peak_voltage already separate most classes in a roughly straight-line way. Good features do a lot of the work before the classifier even sees them.
Why RBF needed tuning to win
RBF's default gamma didn't match the scale of the standardized features, so its flexible boundary either overfit small pockets of training data or underfit real class structure. Once gamma=0.1 was found by search, that same flexibility became an advantage — enough to edge past Linear.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
48

## Slide 50
7. RESULTS & DEEP ANALYSIS
Not All Circuits Are Equally Easy to Diagnose
Chart: 
| RC | RLC | Sallen-Key | RC Ladder
Accuracy | 65.7 | 100 | 82.4 | 60
RLC — 100%
Its oscillatory, underdamped response makes each fault look distinctly different from the others.
RC & RC Ladder — harder
Smoother, more similar-looking passive responses make drift/normal/short faults subtler to tell apart.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
49

## Slide 51
7. RESULTS & DEEP ANALYSIS
Deep Dive: RLC's Perfect Score
Every one of the 5 fault types on the RLC circuit was classified perfectly in the test set:
100%
Normal
100%
Drift
100%
Open
100%
Short
100%
Noise
Why: the RLC circuit's underdamped, oscillatory response is far more distinctive than a passive RC network's smooth curve. An inductance drift shifts the ringing frequency; an open blocks current entirely; a short changes the damping — each fault leaves a very different fingerprint in both the time and frequency domain, which rise_time, dominant_freq and spectral_entropy pick up cleanly.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
50

## Slide 52
7. RESULTS & DEEP ANALYSIS
Deep Dive: Why RC & RC Ladder Are Harder
RC_drift
30%
correct — 60% misread as RC_normal
RC_open
30%
correct — 70% misread as RLC_open (cross-topology)
RC_LADDER_drift
30%
correct — 70% misread as RC_LADDER_normal
RC_LADDER_short
10%
correct — 90% misread as RC_short (cross-topology)
The pattern: passive RC-family circuits produce smoother, less distinctive waveforms than RLC, so drift blends into normal, and a short in one RC-type circuit looks nearly identical to a short in another. This is explored fully in the Confusion Matrix Deep Dive.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
51

## Slide 53
7. RESULTS & DEEP ANALYSIS
What the Model Weighs — and Where It Excels
rise_time and std_voltage carry the most weight in the linear model's decisions.
10 of 20 classes hit a perfect or near-perfect F1 score; RC/RC-Ladder faults trail behind.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
52

## Slide 54
7. RESULTS & DEEP ANALYSIS
Every Prediction, At a Glance
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
53

## Slide 55
7. RESULTS & DEEP ANALYSIS
Confusion Matrix Deep Dive: Three Error Patterns
1. Drift blends into Normal
RC_drift -> RC_normal (6/10), RC_LADDER_drift -> RC_LADDER_normal (7/10), SALLEN_KEY_drift -> SALLEN_KEY_normal (7/11). Expected: drift is defined as a point on the same continuum as normal.
2. Same fault, wrong circuit (same family)
RC_LADDER_short -> RC_short (9/10). Two different passive RC-family circuits produce a nearly identical "instant charge to 5V" waveform when shorted — the model can tell the fault type but not reliably which circuit it's in.
3. A limit the topology rule can't reach
RC_open -> RLC_open (7/10) survives even after correction, because RLC_open is a valid label for an RLC sample — the rule can't know the true circuit is RC without being told, and both faults produce a similarly flat, non-charging output.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
54

## Slide 56
7. RESULTS & DEEP ANALYSIS
Precision vs. Recall: What the Numbers Really Mean
RC_LADDER_short
Precision = 1.000 Recall = 0.100
Every time the model predicts RC_LADDER_short, it's right (precision = 1.0) — but it only catches 1 of every 10 true instances (recall = 0.1), missing the rest by calling them RC_short instead. The model isn't wrong so much as overly cautious about this specific label.
Why this distinction matters
A single accuracy number (78.43%) hides this. F1 combines precision and recall into one score exactly so that a class like this — perfectly precise but rarely triggered — doesn't get miscounted as “working fine.” This is why the Results section leans on F1 and the confusion matrix, not accuracy alone.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
55

## Slide 57
8. KEY FINDING & LIMITS
When Higher Accuracy Is the Wrong Answer
91% -> 76%
reported accuracy, before vs. after removing synthetic data augmentation
An earlier version of this pipeline trained on Python-augmented synthetic data and reported 91% accuracy. Replacing it with pure physics-based LTspice sweep data — real simulation variation, no synthetic shortcuts — dropped accuracy to ~76%. The model hadn't learned circuit fault physics — it had learned to recognise the augmentation transform itself. The lower, honest number is the more trustworthy result.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
56

## Slide 58
8. KEY FINDING & LIMITS
Where the Model Still Struggles
Small per-class test sets
Only ~10 test samples per class — a couple of misses can swing an F1 score sharply (e.g. RC_LADDER_short F1 = 0.18).
Drift is the hardest fault everywhere
Across every circuit, drift is the fault type most often confused with normal — it's inherently a point on a continuum, not a discrete change.
Limited topology scope
Only 4 topologies and 5 fault types studied so far — real analog designs are far more diverse.
Simulation-only validation
Entirely LTspice-based — no real hardware fault injection has been performed yet, so the simulation-to-reality gap is untested.
How uncertain is 78.43%, really? With only 204 test samples, the 95% confidence interval on the headline accuracy is roughly 78.4% ± 5.6 points (binomial standard error) — a reminder that a single test-set number this size deserves a healthy margin of doubt.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
57

## Slide 59
9. DEMO & CONCLUSION
Try It Yourself: Live Web App
APP SCREENSHOT
e.g. screenshot of the Streamlit
dashboard / prediction tab
Dashboard
All results — kernel comparison, per-circuit accuracy, confusion matrix — in one view.
Try Prediction
Pick a sample or enter feature values manually and get an instant fault classification with confidence scores.
Dataset
Browse all 1,019 samples and their 17 extracted features directly in the browser.
analogcircuitsfaultclassification.streamlit.app
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
58

## Slide 60
9. DEMO & CONCLUSION
Tech Stack & Tools
LTspice XVII
Circuit simulation & parameter sweeps
Python
The glue for the entire pipeline
pandas / NumPy
Data wrangling & numeric computation
SciPy
FFT, skewness/kurtosis, interpolation
scikit-learn
SVM, GridSearchCV, StandardScaler
Matplotlib / Seaborn
Results dashboard & confusion matrix
Streamlit
The live interactive web app
Git
Version control across the project
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
59

## Slide 61
9. DEMO & CONCLUSION
Conclusion & What's Next
What We Built
A physics-grounded ML pipeline: LTspice sweeps -> 17 engineered features -> tuned SVM.
78.43% accuracy on a genuinely hard 20-class fault problem.
A novel topology-aware correction rule that adds real accuracy for free.
A live, interactive Streamlit demo anyone can try.
Where It Goes Next
Collect more sweep samples per class to stabilise the weaker F1 scores.
Compare against a 1D-CNN trained directly on raw waveforms.
Validate against real hardware fault injection, not just simulation.
Extend to more topologies — Wien bridge, active high-pass, and beyond.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
60

## Slide 62
Thank You
Questions & discussion welcome.
Karan Kaushik | B.Tech ECE, NIT Silchar Guided by Dr. Anish Kumar Saha SN Bose Summer Internship 2026, NIT Silchar
karankaushik01234@gmail.com
analogcircuitsfaultclassification.streamlit.app

## Slide 63
CODE APPENDIX
Reference: The Project's Source Code
The following slides show the actual Python source files behind every step of this pipeline, presented in the same order the project was built — from raw LTspice parsing through to the deployed web app. These are not meant to be walked through line by line during the talk. They are here purely as backup reference material, in case a reviewer wants to see exactly how a particular step was implemented. Comments are preserved exactly as written in the code.
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
61

## Slide 64
CODE APPENDIX · STEP 1 OF 9
Parsing LTspice Sweeps into a Dataset (1/4)
day12_build_sweep_dataset.py — Reads exported .step sweep files, splits them into individual runs, resamples each to 200 points -> master_dataset_sweep.csv
# day12_build_sweep_dataset.py
# Rebuilds the master dataset from REAL LTspice parameter sweeps.
import os
import numpy as np
import pandas as pd
from scipy.interpolate import interp1d
# ---- Config -------------------------------------------------------
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose\Sweeps"
T_END = {"RC": 0.095, "RLC": 0.095, "RC_LADDER": 0.095, "SALLEN_KEY": 0.020}
N_PTS = 200
CIRCS = ["RC", "RLC", "SALLEN_KEY", "RC_LADDER"]
FAULTS = ["normal", "drift", "open", "short"]
# ---- File finder --------------------------------------------------
def find_sweep_file(folder, circuit, fault):
stems = [
f"{circuit.lower()}_{fault}_sweep",
f"{circuit}_{fault}_sweep",
f"Sallen_key_{fault}_sweep",
f"sallen_key_{fault}_sweep",
]
exts = [".txt", ""]
for s in stems:
for e in exts:
p = os.path.join(folder, s + e)
if os.path.isfile(p) and os.path.getsize(p) > 10_000:
return p
return None
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
62

## Slide 65
CODE APPENDIX · STEP 1 OF 9
Parsing LTspice Sweeps into a Dataset (2/4)
day12_build_sweep_dataset.py (continued)
# ---- Parser -------------------------------------------------------
def parse_step_file(fpath):
runs, cur_t, cur_v, cur_p, prev_t = [], [], [], None, None
def flush():
nonlocal cur_t, cur_v, cur_p
if len(cur_t) > 5:
runs.append((cur_p, np.array(cur_t, dtype=float),
np.array(cur_v, dtype=float)))
cur_t, cur_v = [], []
with open(fpath, "r", errors="ignore") as fh:
for raw in fh:
line = raw.strip()
if not line:
continue
lo = line.lower()
if lo.startswith("step information"):
flush()
try:
cur_p = float(line.split("=")[1].split()[0].rstrip(",)"))
except Exception:
cur_p = np.nan
prev_t = None
continue
if lo.startswith("time") or lo.startswith("step"):
continue
parts = line.replace("\t", " ").replace(",", " ").split()
if len(parts) < 2:
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
63

## Slide 66
CODE APPENDIX · STEP 1 OF 9
Parsing LTspice Sweeps into a Dataset (3/4)
day12_build_sweep_dataset.py (continued)
continue
try:
t, v = float(parts[0]), float(parts[1])
except ValueError:
continue
if prev_t is not None and t < prev_t - 1e-12:
flush()
cur_p = None
cur_t.append(t); cur_v.append(v); prev_t = t
flush()
return runs
# ---- Resample -----------------------------------------------------
def resample(t, v, t_end, n=N_PTS):
grid = np.linspace(0.0, t_end, n)
grid = np.clip(grid, t.min(), t.max())
return interp1d(t, v, kind="linear",
bounds_error=False,
fill_value=(v[0], v[-1]))(grid)
# ---- Build dataset ------------------------------------------------
rows, sid = [], 0
for circ in CIRCS:
cdir = os.path.join(BASE, circ)
for fault in FAULTS:
fpath = find_sweep_file(cdir, circ, fault)
if fpath is None:
print(f"[MISSING] {circ}/{fault} — no file found in {cdir}")
continue
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
64

## Slide 67
CODE APPENDIX · STEP 1 OF 9
Parsing LTspice Sweeps into a Dataset (4/4)
day12_build_sweep_dataset.py (continued)
print(f"[reading] {circ}/{fault}: {os.path.basename(fpath)}"
f" ({os.path.getsize(fpath)//1024} KB)")
runs = parse_step_file(fpath)
print(f" -> {len(runs)} runs parsed")
for pval, t, v in runs:
wave = resample(t, v, T_END[circ])
row = {"sample_id": sid, "circuit": circ,
"fault": fault, "param_value": pval}
row.update({f"v{i}": wave[i] for i in range(N_PTS)})
rows.append(row); sid += 1
df = pd.DataFrame(rows)
out = os.path.join(os.path.dirname(BASE), "master_dataset_sweep.csv")
df.to_csv(out, index=False)
print(f"\n{'='*50}")
print(f"Saved {len(df)} samples -> {out}")
print(f"Columns: {len(df.columns)}")
print(f"\nSamples per class:")
print(df.groupby(["circuit", "fault"]).size().to_string())
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
65

## Slide 68
CODE APPENDIX · STEP 2 OF 9
Generating Noise-Fault Samples (1/2)
day12b_generate_noise_samples.py — Adds seeded Gaussian noise (SNR = 25 dB) onto NORMAL waveforms to create the fifth fault class
# day12b_generate_noise_samples.py
# Generates noise-fault samples per circuit by injecting
# Gaussian noise onto the NORMAL sweep waveforms.
# Noise is physically justified: real circuit noise is stochastic,
# not a deterministic component shift.
import os
import numpy as np
import pandas as pd
# ---- Config -------------------------------------------------------
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
CSV_IN = os.path.join(BASE, "master_dataset_sweep.csv")
SNR_DB = 25
SEED = 42
CIRCUITS = ["RC", "RLC", "SALLEN_KEY", "RC_LADDER"]
N_PTS = 200
rng = np.random.default_rng(SEED)
# ---- Load existing dataset ----------------------------------------
df = pd.read_csv(CSV_IN)
wave_cols = [f"v{i}" for i in range(N_PTS)]
next_id = df["sample_id"].max() + 1
noise_rows = []
for circ in CIRCUITS:
normals = df[(df["circuit"] == circ) & (df["fault"] == "normal")]
n_noise = len(normals) # match exactly — 51 per circuit
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
66

## Slide 69
CODE APPENDIX · STEP 2 OF 9
Generating Noise-Fault Samples (2/2)
day12b_generate_noise_samples.py (continued)
normal_waves = normals[wave_cols].values
for i in range(n_noise):
base = normal_waves[i % len(normal_waves)]
sig_power = np.mean(base ** 2)
noise_power = sig_power / (10 ** (SNR_DB / 10))
noise_std = np.sqrt(noise_power)
noisy = base + rng.normal(0, noise_std, size=N_PTS)
row = {
"sample_id": next_id,
"circuit": circ,
"fault": "noise",
"param_value": SNR_DB
}
row.update({f"v{i}": noisy[i] for i in range(N_PTS)})
noise_rows.append(row)
next_id += 1
print(f"{circ}/noise: {n_noise} samples generated at {SNR_DB} dB SNR")
# ---- Append and save ----------------------------------------------
df_noise = pd.DataFrame(noise_rows)
df_final = pd.concat([df, df_noise], ignore_index=True)
out = os.path.join(BASE, "master_dataset_sweep.csv")
df_final.to_csv(out, index=False)
print(f"\nFinal dataset: {len(df_final)} samples")
print(df_final.groupby(["circuit", "fault"]).size().to_string())
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
67

## Slide 70
CODE APPENDIX · STEP 3 OF 9
Extracting 17 Features per Waveform (1/5)
day13_v2.py — Turns each 200-point waveform into the 17 time-, frequency-domain and structural features -> features_v2.csv
﻿# day13_feature_extraction_v2.py
# Extracts 17 features (16 original + f17_dc_level) from every waveform.
# f17_dc_level = mean of last 20 points — directly separates RC_open (near 0V)
# from RC_short (near 5V), fixing the F1=0 failure identified in Day 16.
import os
import numpy as np
import pandas as pd
from scipy.stats import skew, kurtosis
from scipy.fft import rfft, rfftfreq
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
CSV_IN = os.path.join(BASE, "master_dataset_sweep.csv")
CSV_OUT = os.path.join(BASE, "features_v2.csv")
N_PTS = 200
T_END = {
"RC": 0.095,
"RLC": 0.095,
"RC_LADDER": 0.095,
"SALLEN_KEY": 0.020
}
def f1_peak_voltage(v): return float(np.max(v))
def f2_rms_value(v): return float(np.sqrt(np.mean(v**2)))
def f3_mean_voltage(v): return float(np.mean(v))
def f4_std_voltage(v): return float(np.std(v))
def f5_rise_time(t, v):
peak = np.max(v)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
68

## Slide 71
CODE APPENDIX · STEP 3 OF 9
Extracting 17 Features per Waveform (2/5)
day13_v2.py (continued)
if peak < 1e-6: return float(t[-1])
idx_lo = np.argmax(v >= 0.1*peak)
idx_hi = np.argmax(v >= 0.9*peak)
if idx_hi <= idx_lo: return float(t[-1]-t[0])
return float(t[idx_hi]-t[idx_lo])
def f6_settling_time(t, v):
final = v[-1]
if abs(final) < 1e-6: return float(t[-1])
outside = np.where(np.abs(v-final) > 0.02*abs(final))[0]
if len(outside)==0: return float(t[0])
return float(t[outside[-1]])
def f7_skewness(v): return float(skew(v))
def f8_kurtosis(v): return float(kurtosis(v))
def f9_dominant_freq(v, t_end, n):
dt=t_end/(n-1); freq=rfftfreq(n,d=dt); mag=np.abs(rfft(v))
mask=(freq>=50)&(freq<=2000)
if not np.any(mask): return float(freq[np.argmax(mag)])
return float(freq[mask][np.argmax(mag[mask])])
def f10_spectral_energy(v, t_end, n):
mag=np.abs(rfft(v)); return float(np.sum(mag**2))
def f11_spectral_centroid(v, t_end, n):
dt=t_end/(n-1); freq=rfftfreq(n,d=dt); mag=np.abs(rfft(v))
denom=np.sum(mag)
if denom<1e-12: return 0.0
return float(np.sum(freq*mag)/denom)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
69

## Slide 72
CODE APPENDIX · STEP 3 OF 9
Extracting 17 Features per Waveform (3/5)
day13_v2.py (continued)
def f12_bandwidth(v, t_end, n):
dt=t_end/(n-1); freq=rfftfreq(n,d=dt); mag=np.abs(rfft(v))
denom=np.sum(mag)
if denom<1e-12: return 0.0
c=np.sum(freq*mag)/denom
return float(np.sqrt(np.sum(((freq-c)**2)*mag)/denom))
def f13_spectral_entropy(v, t_end, n):
mag=np.abs(rfft(v))**2; total=np.sum(mag)
if total<1e-12: return 0.0
p=mag/total; p=p[p>0]
return float(-np.sum(p*np.log2(p)))
def f14_energy(v): return float(np.sum(v**2))
def f15_zero_crossing_rate(v):
return float(np.sum(np.diff(np.sign(v-np.mean(v)))!=0)/len(v))
def f16_crest_factor(v):
rms=np.sqrt(np.mean(v**2))
if rms<1e-12: return 0.0
return float(np.max(np.abs(v))/rms)
def f17_dc_level(v):
# Mean of last 20 points = steady-state DC level.
# RC_open: near 0V (capacitor never charges in 95ms window)
# RC_short: near 5V (capacitor charges instantly)
# This directly separates the two previously confused classes.
return float(np.mean(v[-20:]))
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
70

## Slide 73
CODE APPENDIX · STEP 3 OF 9
Extracting 17 Features per Waveform (4/5)
day13_v2.py (continued)
df_raw = pd.read_csv(CSV_IN)
wave_cols = [f"v{i}" for i in range(N_PTS)]
records = []
for idx, row in df_raw.iterrows():
circ = row["circuit"]
t_end = T_END[circ]
v = row[wave_cols].values.astype(float)
t = np.linspace(0.0, t_end, N_PTS)
rec = {
"sample_id": int(row["sample_id"]),
"circuit": circ,
"fault": row["fault"],
"f1": f1_peak_voltage(v),
"f2": f2_rms_value(v),
"f3": f3_mean_voltage(v),
"f4": f4_std_voltage(v),
"f5": f5_rise_time(t,v),
"f6": f6_settling_time(t,v),
"f7": f7_skewness(v),
"f8": f8_kurtosis(v),
"f9": f9_dominant_freq(v,t_end,N_PTS),
"f10": f10_spectral_energy(v,t_end,N_PTS),
"f11": f11_spectral_centroid(v,t_end,N_PTS),
"f12": f12_bandwidth(v,t_end,N_PTS),
"f13": f13_spectral_entropy(v,t_end,N_PTS),
"f14": f14_energy(v),
"f15": f15_zero_crossing_rate(v),
"f16": f16_crest_factor(v),
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
71

## Slide 74
CODE APPENDIX · STEP 3 OF 9
Extracting 17 Features per Waveform (5/5)
day13_v2.py (continued)
"f17": f17_dc_level(v), } records.append(rec) if (idx+1)%100==0: print(f" processed {idx+1}/{len(df_raw)}...") df_feat = pd.DataFrame(records) df_feat.to_csv(CSV_OUT, index=False) print(f"\nSaved {len(df_feat)} rows -> {CSV_OUT}") print(f"Columns: {len(df_feat.columns)} (sample_id + circuit + fault + f1-f17)") # Quick diagnosis: RC_open vs RC_short on f17 rc_open = df_feat[(df_feat["circuit"]=="RC")&(df_feat["fault"]=="open")]["f17"].mean() rc_short = df_feat[(df_feat["circuit"]=="RC")&(df_feat["fault"]=="short")]["f17"].mean() print(f"\nf17 diagnosis:") print(f" RC_open mean dc_level = {rc_open:.4f} V") print(f" RC_short mean dc_level = {rc_short:.4f} V") print(f" Separation gap = {abs(rc_open-rc_short):.4f} V") print(f" Separable: {'YES' if abs(rc_open-rc_short) > 1.0 else 'MARGINAL'}")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
72

## Slide 75
CODE APPENDIX · STEP 4 OF 9
Baseline SVM Training (Default Hyperparameters) (1/4)
day14_svm_baseline.py — Trains Linear / RBF / Polynomial kernels with near-default settings — the Section 5 baseline numbers come from here
# day14_svm_baseline.py
# Honest SVM baseline on real LTspice sweep features.
# Trains Linear, RBF, and Polynomial SVMs on features.csv
# and reports per-class and overall performance.
import os
import numpy as np
import pandas as pd
from sklearn.svm import SVC
from sklearn.preprocessing import StandardScaler, LabelEncoder
from sklearn.model_selection import train_test_split, cross_val_score
from sklearn.metrics import (accuracy_score, classification_report,
confusion_matrix)
import warnings
warnings.filterwarnings("ignore")
# ---- Config -------------------------------------------------------
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
CSV_IN = os.path.join(BASE, "features.csv")
OUT_FILE = os.path.join(BASE, "day14_results.txt")
FEATURE_COLS = [f"f{i}" for i in range(1, 17)]
RANDOM_STATE = 42
TEST_SIZE = 0.20
# ---- Load data ----------------------------------------------------
df = pd.read_csv(CSV_IN)
print(f"Loaded {len(df)} samples, {len(FEATURE_COLS)} features")
print(f"Classes: {sorted(df['fault'].unique())}")
print(f"Circuits: {sorted(df['circuit'].unique())}\n")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
73

## Slide 76
CODE APPENDIX · STEP 4 OF 9
Baseline SVM Training (Default Hyperparameters) (2/4)
day14_svm_baseline.py (continued)
# Create combined label: circuit_fault (20 classes)
df["label"] = df["circuit"] + "_" + df["fault"]
print(f"Total unique labels: {df['label'].nunique()}")
print(df.groupby("label").size().to_string())
print()
# ---- Encode and split ---------------------------------------------
le = LabelEncoder()
y = le.fit_transform(df["label"])
X = df[FEATURE_COLS].values
X_train, X_test, y_train, y_test = train_test_split(
X, y, test_size=TEST_SIZE, random_state=RANDOM_STATE, stratify=y
)
print(f"Train: {len(X_train)} samples | Test: {len(X_test)} samples\n")
# ---- Scale --------------------------------------------------------
scaler = StandardScaler()
X_train = scaler.fit_transform(X_train)
X_test = scaler.transform(X_test)
# ---- Define three kernels -----------------------------------------
kernels = {
"Linear": SVC(kernel="linear", C=1.0,
random_state=RANDOM_STATE, decision_function_shape="ovo"),
"RBF": SVC(kernel="rbf", C=1.0, gamma="scale",
random_state=RANDOM_STATE, decision_function_shape="ovo"),
"Polynomial": SVC(kernel="poly", C=1.0, gamma="scale", degree=3, coef0=1,
random_state=RANDOM_STATE, decision_function_shape="ovo"),
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
74

## Slide 77
CODE APPENDIX · STEP 4 OF 9
Baseline SVM Training (Default Hyperparameters) (3/4)
day14_svm_baseline.py (continued)
} # ---- Train, evaluate, report -------------------------------------- results = {} output_lines = [] def log(line=""): print(line) output_lines.append(line) log("=" * 60) log("DAY 14 — SVM BASELINE ON REAL SWEPT DATA") log("=" * 60) log(f"Dataset : {len(df)} samples | {len(FEATURE_COLS)} features | 20 classes") log(f"Split : {int((1-TEST_SIZE)*100)}% train / {int(TEST_SIZE*100)}% test | stratified") log(f"Scaling : StandardScaler (zero mean, unit variance)") log() for name, clf in kernels.items(): log(f"{'─'*60}") log(f"KERNEL: {name}") log(f"{'─'*60}") # Train clf.fit(X_train, y_train) # Test accuracy y_pred = clf.predict(X_test) test_acc = accuracy_score(y_test, y_pred)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
75

## Slide 78
CODE APPENDIX · STEP 4 OF 9
Baseline SVM Training (Default Hyperparameters) (4/4)
day14_svm_baseline.py (continued)
# 5-fold cross-validation on full dataset cv_scores = cross_val_score(clf, X_train, y_train, cv=5, scoring="accuracy") log(f"Test Accuracy : {test_acc*100:.2f}%") log(f"CV Accuracy : {cv_scores.mean()*100:.2f}% ± {cv_scores.std()*100:.2f}%") log() # Per-class report report = classification_report( y_test, y_pred, target_names=le.classes_, digits=3 ) log("Classification Report:") log(report)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
76

## Slide 79
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (1/8)
day15_gridsearch.py — Exhaustive grid search over C, gamma and degree for each kernel, scored with 5-fold cross-validation
# day15_gridsearch.py
# GridSearchCV hyperparameter tuning for Linear, RBF, and Polynomial SVMs.
# Finds optimal C, gamma, degree for each kernel.
# Test set never touched during search — only used for final evaluation.
import os
import numpy as np
import pandas as pd
from sklearn.svm import SVC
from sklearn.preprocessing import StandardScaler, LabelEncoder
from sklearn.model_selection import train_test_split, GridSearchCV
from sklearn.metrics import accuracy_score, classification_report
import warnings
warnings.filterwarnings("ignore")
# ---- Config -------------------------------------------------------
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
CSV_IN = os.path.join(BASE, "features.csv")
OUT_FILE = os.path.join(BASE, "day15_results.txt")
FEATURE_COLS = [f"f{i}" for i in range(1, 17)]
RANDOM_STATE = 42
TEST_SIZE = 0.20
CV_FOLDS = 5
# Day 14 baseline for comparison
DAY14 = {"Linear": 76.47, "RBF": 70.59, "Polynomial": 74.02}
# ---- Search grids -------------------------------------------------
# Wide log-scale search for C and gamma
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
77

## Slide 80
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (2/8)
day15_gridsearch.py (continued)
PARAM_GRIDS = {
"Linear": {
"C": [0.001, 0.01, 0.1, 1, 10, 100, 1000]
},
"RBF": {
"C": [0.1, 1, 10, 100, 1000],
"gamma": [0.0001, 0.001, 0.01, 0.1, 1, 10]
},
"Polynomial": {
"C": [0.1, 1, 10, 100],
"gamma": [0.001, 0.01, 0.1],
"degree": [2, 3],
"coef0": [1]
}
}
# ---- Load and prepare ---------------------------------------------
df = pd.read_csv(CSV_IN)
df["label"] = df["circuit"] + "_" + df["fault"]
le = LabelEncoder()
y = le.fit_transform(df["label"])
X = df[FEATURE_COLS].values
X_train, X_test, y_train, y_test = train_test_split(
X, y, test_size=TEST_SIZE, random_state=RANDOM_STATE, stratify=y
)
scaler = StandardScaler()
X_train = scaler.fit_transform(X_train)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
78

## Slide 81
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (3/8)
day15_gridsearch.py (continued)
X_test = scaler.transform(X_test)
print(f"Train: {len(X_train)} | Test: {len(X_test)}")
print(f"Search grids:")
for k, g in PARAM_GRIDS.items():
n = 1
for v in g.values(): n *= len(v)
print(f" {k}: {n} combinations × {CV_FOLDS} folds = {n*CV_FOLDS} fits")
print()
# ---- Run GridSearchCV ---------------------------------------------
output_lines = []
def log(line=""):
print(line)
output_lines.append(line)
log("=" * 60)
log("DAY 15 — GRIDSEARCHCV HYPERPARAMETER TUNING")
log("=" * 60)
log(f"Dataset : 1019 samples | 16 features | 20 classes")
log(f"Split : 80/20 stratified | CV folds: {CV_FOLDS}")
log()
tuned_results = {}
# Linear
log("─" * 60)
log("KERNEL: Linear")
log("─" * 60)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
79

## Slide 82
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (4/8)
day15_gridsearch.py (continued)
log(f"Search grid: C = {PARAM_GRIDS['Linear']['C']}")
gs_linear = GridSearchCV(
SVC(kernel="linear", decision_function_shape="ovo",
random_state=RANDOM_STATE),
param_grid={"C": PARAM_GRIDS["Linear"]["C"]},
cv=CV_FOLDS, scoring="accuracy", n_jobs=-1, verbose=1
)
gs_linear.fit(X_train, y_train)
best_linear = gs_linear.best_estimator_
y_pred = best_linear.predict(X_test)
test_acc = accuracy_score(y_test, y_pred)
log(f"Best params : C = {gs_linear.best_params_['C']}")
log(f"Best CV acc : {gs_linear.best_score_*100:.2f}%")
log(f"Test acc : {test_acc*100:.2f}% (Day14 default: {DAY14['Linear']}%)")
log(f"Improvement : {(test_acc*100 - DAY14['Linear']):+.2f}%")
log()
log("Classification Report:")
log(classification_report(y_test, y_pred,
target_names=le.classes_, digits=3))
tuned_results["Linear"] = {
"best_params": gs_linear.best_params_,
"best_cv": gs_linear.best_score_,
"test_acc": test_acc,
"report": classification_report(y_test, y_pred,
target_names=le.classes_, digits=3)
}
# RBF
log("─" * 60)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
80

## Slide 83
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (5/8)
day15_gridsearch.py (continued)
log("KERNEL: RBF")
log("─" * 60)
log(f"Search grid: C = {PARAM_GRIDS['RBF']['C']}, "
f"gamma = {PARAM_GRIDS['RBF']['gamma']}")
gs_rbf = GridSearchCV(
SVC(kernel="rbf", decision_function_shape="ovo",
random_state=RANDOM_STATE),
param_grid={"C": PARAM_GRIDS["RBF"]["C"],
"gamma": PARAM_GRIDS["RBF"]["gamma"]},
cv=CV_FOLDS, scoring="accuracy", n_jobs=-1, verbose=1
)
gs_rbf.fit(X_train, y_train)
best_rbf = gs_rbf.best_estimator_
y_pred = best_rbf.predict(X_test)
test_acc = accuracy_score(y_test, y_pred)
log(f"Best params : C = {gs_rbf.best_params_['C']}, "
f"gamma = {gs_rbf.best_params_['gamma']}")
log(f"Best CV acc : {gs_rbf.best_score_*100:.2f}%")
log(f"Test acc : {test_acc*100:.2f}% (Day14 default: {DAY14['RBF']}%)")
log(f"Improvement : {(test_acc*100 - DAY14['RBF']):+.2f}%")
log()
log("Classification Report:")
log(classification_report(y_test, y_pred,
target_names=le.classes_, digits=3))
tuned_results["RBF"] = {
"best_params": gs_rbf.best_params_,
"best_cv": gs_rbf.best_score_,
"test_acc": test_acc,
"report": classification_report(y_test, y_pred,
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
81

## Slide 84
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (6/8)
day15_gridsearch.py (continued)
target_names=le.classes_, digits=3)
}
# Polynomial
log("─" * 60)
log("KERNEL: Polynomial")
log("─" * 60)
log(f"Search grid: C={PARAM_GRIDS['Polynomial']['C']}, "
f"gamma={PARAM_GRIDS['Polynomial']['gamma']}, "
f"degree={PARAM_GRIDS['Polynomial']['degree']}")
gs_poly = GridSearchCV(
SVC(kernel="poly", decision_function_shape="ovo",
random_state=RANDOM_STATE),
param_grid={"C": PARAM_GRIDS["Polynomial"]["C"],
"gamma": PARAM_GRIDS["Polynomial"]["gamma"],
"degree": PARAM_GRIDS["Polynomial"]["degree"],
"coef0": PARAM_GRIDS["Polynomial"]["coef0"]},
cv=CV_FOLDS, scoring="accuracy", n_jobs=-1, verbose=1
)
gs_poly.fit(X_train, y_train)
best_poly = gs_poly.best_estimator_
y_pred = best_poly.predict(X_test)
test_acc = accuracy_score(y_test, y_pred)
log(f"Best params : C={gs_poly.best_params_['C']}, "
f"gamma={gs_poly.best_params_['gamma']}, "
f"degree={gs_poly.best_params_['degree']}, "
f"coef0={gs_poly.best_params_['coef0']}")
log(f"Best CV acc : {gs_poly.best_score_*100:.2f}%")
log(f"Test acc : {test_acc*100:.2f}% (Day14 default: {DAY14['Polynomial']}%)")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
82

## Slide 85
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (7/8)
day15_gridsearch.py (continued)
log(f"Improvement : {(test_acc*100 - DAY14['Polynomial']):+.2f}%")
log()
log("Classification Report:")
log(classification_report(y_test, y_pred,
target_names=le.classes_, digits=3))
tuned_results["Polynomial"] = {
"best_params": gs_poly.best_params_,
"best_cv": gs_poly.best_score_,
"test_acc": test_acc,
"report": classification_report(y_test, y_pred,
target_names=le.classes_, digits=3)
}
# ---- Final summary ------------------------------------------------
log("=" * 60)
log("FINAL SUMMARY — DEFAULT vs TUNED")
log("=" * 60)
log(f"{'Kernel':<14} {'Default':>10} {'Tuned':>10} {'Gain':>10} {'Best Params'}")
log(f"{'─'*14} {'─'*10} {'─'*10} {'─'*10} {'─'*30}")
for name, r in tuned_results.items():
gain = r['test_acc']*100 - DAY14[name]
params_str = ", ".join(f"{k}={v}" for k,v in r['best_params'].items())
log(f"{name:<14} {DAY14[name]:>9.2f}% "
f"{r['test_acc']*100:>9.2f}% "
f"{gain:>+9.2f}% "
f"{params_str}")
log()
best_kernel = max(tuned_results, key=lambda k: tuned_results[k]['test_acc'])
log(f"Best overall kernel (tuned): {best_kernel} at "
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
83

## Slide 86
CODE APPENDIX · STEP 5 OF 9
Hyperparameter Tuning with GridSearchCV (8/8)
day15_gridsearch.py (continued)
f"{tuned_results[best_kernel]['test_acc']*100:.2f}%") # ---- Save --------------------------------------------------------- with open(OUT_FILE, "w", encoding="utf-8") as f: f.write("\n".join(output_lines)) print(f"\nResults saved -> {OUT_FILE}")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
84

## Slide 87
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (1/7)
day16_confusion_analysis.py — Generates the confusion matrix, per-class F1 chart, and the RC_open vs. RC_short / Normal vs. Drift feature diagnosis
# day16_confusion_analysis.py
# Full confusion matrix analysis and error diagnosis
# using the best model from Day 15: RBF C=100, gamma=0.1
import os
import numpy as np
import pandas as pd
import matplotlib
matplotlib.use('Agg') # non-interactive backend for saving
import matplotlib.pyplot as plt
import seaborn as sns
from sklearn.svm import SVC
from sklearn.preprocessing import StandardScaler, LabelEncoder
from sklearn.model_selection import train_test_split
from sklearn.metrics import (accuracy_score, classification_report,
confusion_matrix, f1_score)
import warnings
warnings.filterwarnings("ignore")
# ---- Config -------------------------------------------------------
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
CSV_IN = os.path.join(BASE, "features.csv")
OUT_DIR = os.path.join(BASE, "Day16_Analysis")
os.makedirs(OUT_DIR, exist_ok=True)
FEATURE_COLS = [f"f{i}" for i in range(1, 17)]
RANDOM_STATE = 42
TEST_SIZE = 0.20
# ---- Load and prepare ---------------------------------------------
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
85

## Slide 88
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (2/7)
day16_confusion_analysis.py (continued)
df = pd.read_csv(CSV_IN)
df["label"] = df["circuit"] + "_" + df["fault"]
le = LabelEncoder()
y = le.fit_transform(df["label"])
X = df[FEATURE_COLS].values
X_train, X_test, y_train, y_test = train_test_split(
X, y, test_size=TEST_SIZE, random_state=RANDOM_STATE, stratify=y
)
scaler = StandardScaler()
X_train = scaler.fit_transform(X_train)
X_test = scaler.transform(X_test)
# ---- Train best model (RBF tuned) ---------------------------------
print("Training best model: RBF C=100, gamma=0.1 ...")
clf = SVC(kernel="rbf", C=100, gamma=0.1,
decision_function_shape="ovo", random_state=RANDOM_STATE)
clf.fit(X_train, y_train)
y_pred = clf.predict(X_test)
test_acc = accuracy_score(y_test, y_pred)
print(f"Test accuracy: {test_acc*100:.2f}%\n")
# ---- 1. Full 20x20 Confusion Matrix heatmap -----------------------
print("Generating confusion matrix heatmap...")
cm = confusion_matrix(y_test, y_pred)
labels = le.classes_
fig, ax = plt.subplots(figsize=(18, 15))
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
86

## Slide 89
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (3/7)
day16_confusion_analysis.py (continued)
sns.heatmap(cm, annot=True, fmt='d', cmap='Blues',
xticklabels=labels, yticklabels=labels,
linewidths=0.5, ax=ax)
ax.set_xlabel("Predicted Label", fontsize=12)
ax.set_ylabel("True Label", fontsize=12)
ax.set_title(f"Confusion Matrix — RBF SVM (C=100, γ=0.1)\nTest Accuracy: {test_acc*100:.2f}%",
fontsize=14)
plt.xticks(rotation=45, ha='right', fontsize=8)
plt.yticks(rotation=0, fontsize=8)
plt.tight_layout()
path1 = os.path.join(OUT_DIR, "confusion_matrix.png")
plt.savefig(path1, dpi=150, bbox_inches='tight')
plt.close()
print(f"Saved: {path1}")
# ---- 2. Per-class F1 bar chart ------------------------------------
print("Generating per-class F1 chart...")
f1_scores = f1_score(y_test, y_pred, average=None)
f1_df = pd.DataFrame({"class": labels, "f1": f1_scores})
f1_df = f1_df.sort_values("f1", ascending=True)
colors = ["#d32f2f" if f < 0.5 else "#f57c00" if f < 0.8
else "#388e3c" for f in f1_df["f1"]]
fig, ax = plt.subplots(figsize=(12, 8))
bars = ax.barh(f1_df["class"], f1_df["f1"], color=colors)
ax.axvline(x=0.5, color='red', linestyle='--', alpha=0.5, label='F1=0.5 threshold')
ax.axvline(x=0.8, color='orange', linestyle='--', alpha=0.5, label='F1=0.8 threshold')
for bar, val in zip(bars, f1_df["f1"]):
ax.text(bar.get_width() + 0.01, bar.get_y() + bar.get_height()/2,
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
87

## Slide 90
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (4/7)
day16_confusion_analysis.py (continued)
f'{val:.3f}', va='center', fontsize=9)
ax.set_xlabel("F1 Score", fontsize=12)
ax.set_title("Per-Class F1 Score — RBF SVM (C=100, γ=0.1)", fontsize=14)
ax.set_xlim(0, 1.15)
ax.legend(fontsize=10)
plt.tight_layout()
path2 = os.path.join(OUT_DIR, "f1_per_class.png")
plt.savefig(path2, dpi=150, bbox_inches='tight')
plt.close()
print(f"Saved: {path2}")
# ---- 3. Top confused pairs ----------------------------------------
print("\nTop 10 most confused class pairs:")
print(f"{'Actual':<25} {'Predicted':<25} {'Count':>6}")
print("-" * 58)
confused = []
for i in range(len(labels)):
for j in range(len(labels)):
if i != j and cm[i, j] > 0:
confused.append((labels[i], labels[j], cm[i, j]))
confused.sort(key=lambda x: -x[2])
for actual, predicted, count in confused[:10]:
print(f"{actual:<25} {predicted:<25} {count:>6}")
# ---- 4. Per-circuit accuracy breakdown ----------------------------
print("\nPer-circuit accuracy:")
print(f"{'Circuit':<15} {'Accuracy':>10} {'Correct':>8} {'Total':>8}")
print("-" * 45)
# Map test indices back to circuit labels
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
88

## Slide 91
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (5/7)
day16_confusion_analysis.py (continued)
df_test = df.iloc[
pd.Series(range(len(df))).sample(frac=TEST_SIZE,
random_state=RANDOM_STATE).sort_values().index
]
circuits = ["RC", "RLC", "SALLEN_KEY", "RC_LADDER"]
y_test_labels = le.inverse_transform(y_test)
y_pred_labels = le.inverse_transform(y_pred)
for circ in circuits:
mask = np.array([circ + "_" in l for l in y_test_labels])
if mask.sum() == 0:
continue
correct = np.sum(y_test_labels[mask] == y_pred_labels[mask])
total = mask.sum()
acc = correct / total * 100
print(f"{circ:<15} {acc:>9.2f}% {correct:>8} {total:>8}")
# ---- 5. RC_open diagnosis -----------------------------------------
print("\n--- RC_open vs RC_short Feature Diagnosis ---")
rc_open = df[(df["circuit"]=="RC") & (df["fault"]=="open")]
rc_short = df[(df["circuit"]=="RC") & (df["fault"]=="short")]
key_features = ["f1", "f2", "f3", "f4", "f5", "f14"]
feat_names = {
"f1": "peak_voltage", "f2": "rms_value",
"f3": "mean_voltage", "f4": "std_voltage",
"f5": "rise_time", "f14": "energy"
}
print(f"\n{'Feature':<12} {'RC_open mean':>14} {'RC_short mean':>14} {'Separable?':>12}")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
89

## Slide 92
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (6/7)
day16_confusion_analysis.py (continued)
print("-" * 55)
for f in key_features:
o_mean = rc_open[f].mean()
s_mean = rc_short[f].mean()
gap = abs(o_mean - s_mean)
sep = "YES" if gap > 0.5 else "MARGINAL" if gap > 0.1 else "NO"
print(f"{feat_names[f]:<12} {o_mean:>14.4f} {s_mean:>14.4f} {sep:>12}")
# ---- 6. Normal vs Drift diagnosis ---------------------------------
print("\n--- Normal vs Drift Feature Diagnosis (all circuits) ---")
normal = df[df["fault"]=="normal"]
drift = df[df["fault"]=="drift"]
print(f"\n{'Feature':<12} {'Normal mean':>13} {'Drift mean':>13} {'Separable?':>12}")
print("-" * 52)
for f in ["f1","f2","f3","f5","f6","f9","f13"]:
n_mean = normal[f].mean()
d_mean = drift[f].mean()
gap = abs(n_mean - d_mean)
sep = "YES" if gap > 0.5 else "MARGINAL" if gap > 0.1 else "NO"
print(f"{f:<12} {n_mean:>13.4f} {d_mean:>13.4f} {sep:>12}")
# ---- 7. Summary report --------------------------------------------
report = classification_report(y_test, y_pred,
target_names=labels, digits=3)
print(f"\nFull Classification Report:\n{report}")
summary = f"""
DAY 16 ANALYSIS SUMMARY
========================
Best Model : RBF SVM, C=100, gamma=0.1
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
90

## Slide 93
CODE APPENDIX · STEP 6 OF 9
Confusion Matrix & Diagnostic Analysis (7/7)
day16_confusion_analysis.py (continued)
Test Accuracy : {test_acc*100:.2f}%
Perfect classes (F1=1.0):
{', '.join([labels[i] for i,f in enumerate(f1_scores) if f==1.0])}
Failed classes (F1=0):
{', '.join([labels[i] for i,f in enumerate(f1_scores) if f==0.0])}
Weak classes (F1 < 0.5):
{', '.join([labels[i] for i,f in enumerate(f1_scores) if 0 < f < 0.5])}
"""
print(summary)
out_txt = os.path.join(OUT_DIR, "day16_summary.txt")
with open(out_txt, "w", encoding="utf-8") as f:
f.write(summary)
f.write("\nFull Classification Report:\n")
f.write(report)
f.write("\n\nTop Confused Pairs:\n")
for actual, predicted, count in confused[:10]:
f.write(f"{actual} -> {predicted}: {count}\n")
print(f"\nAll outputs saved to: {OUT_DIR}")
print("Files: confusion_matrix.png, f1_per_class.png, day16_summary.txt")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
91

## Slide 94
CODE APPENDIX · STEP 7 OF 9
Training & Saving the Final Deployment Model (1/2)
save_model.py — Fits the final tuned RBF model on features_v2.csv and serializes model.pkl / scaler.pkl / label_encoder.pkl
# save_model.py
# Trains the final RBF model with topology rule and saves it
# as .pkl files for deployment in the Streamlit app.
import os, warnings
warnings.filterwarnings('ignore')
import numpy as np, pandas as pd
import joblib
from sklearn.svm import SVC
from sklearn.preprocessing import StandardScaler, LabelEncoder
from sklearn.model_selection import train_test_split
BASE = r"C:\Users\karan\Desktop\May-June_july\Final Sn Bose"
FEATURE_COLS = [f"f{i}" for i in range(1, 18)]
# Load data
df = pd.read_csv(os.path.join(BASE, "features_v2.csv"))
df["label"] = df["circuit"] + "_" + df["fault"]
# Encode labels
le = LabelEncoder()
y = le.fit_transform(df["label"])
X = df[FEATURE_COLS].values
# Split (same random_state as before for consistency)
X_train, X_test, y_train, y_test = train_test_split(
X, y, test_size=0.20, random_state=42, stratify=y
)
# Scale
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
92

## Slide 95
CODE APPENDIX · STEP 7 OF 9
Training & Saving the Final Deployment Model (2/2)
save_model.py (continued)
scaler = StandardScaler()
X_train_scaled = scaler.fit_transform(X_train)
X_test_scaled = scaler.transform(X_test)
# Train final model
model = SVC(kernel="rbf", C=100, gamma=0.1,
decision_function_shape="ovo", random_state=42, probability=True)
model.fit(X_train_scaled, y_train)
# Verify accuracy
from sklearn.metrics import accuracy_score
acc = accuracy_score(y_test, model.predict(X_test_scaled)) * 100
print(f"Model accuracy on test set: {acc:.2f}%")
# Save everything needed for deployment
SAVE_DIR = os.path.join(BASE, "deployment")
os.makedirs(SAVE_DIR, exist_ok=True)
joblib.dump(model, os.path.join(SAVE_DIR, "model.pkl"))
joblib.dump(scaler, os.path.join(SAVE_DIR, "scaler.pkl"))
joblib.dump(le, os.path.join(SAVE_DIR, "label_encoder.pkl"))
# Also save a few sample test rows for the demo
sample_df = df.iloc[X_test.shape[0]*0:5].copy() # first 5 rows for demo
sample_df.to_csv(os.path.join(SAVE_DIR, "sample_input.csv"), index=False)
print(f"\nSaved to: {SAVE_DIR}")
print("Files: model.pkl, scaler.pkl, label_encoder.pkl, sample_input.csv")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
93

## Slide 96
CODE APPENDIX · STEP 8 OF 9
Generating the Results Dashboard (1/5)
regenerate_dashboard.py — Builds the 6-panel results_dashboard_FINAL.png used throughout the Results section of this deck
﻿import os, warnings
warnings.filterwarnings('ignore')
import numpy as np, pandas as pd
import matplotlib; matplotlib.use('Agg')
import matplotlib.pyplot as plt
import matplotlib.gridspec as gridspec
import seaborn as sns
from sklearn.svm import SVC
from sklearn.preprocessing import StandardScaler, LabelEncoder
from sklearn.model_selection import train_test_split
from sklearn.metrics import accuracy_score, f1_score, confusion_matrix, classification_report
REPO = r"C:\Users\karan\Desktop\fault-classification-project"
OUT_DIR = os.path.join(REPO, "results")
os.makedirs(OUT_DIR, exist_ok=True)
FEATURE_COLS = [f'f{i}' for i in range(1,18)]
FEATURE_NAMES = ['peak_voltage','rms_value','mean_voltage','std_voltage',
'rise_time','settling_time','skewness','kurtosis','dominant_freq',
'spectral_energy','spec_centroid','bandwidth','spec_entropy','energy',
'zero_crossing_rate','crest_factor','dc_level']
df = pd.read_csv(os.path.join(REPO, "data", "features_v2.csv"))
df['label'] = df['circuit'] + '_' + df['fault']
le = LabelEncoder()
y = le.fit_transform(df['label'])
X = df[FEATURE_COLS].values
X_tr, X_te, y_tr, y_te = train_test_split(X, y, test_size=0.2, random_state=42, stratify=y)
sc = StandardScaler()
X_tr = sc.fit_transform(X_tr)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
94

## Slide 97
CODE APPENDIX · STEP 8 OF 9
Generating the Results Dashboard (2/5)
regenerate_dashboard.py (continued)
X_te = sc.transform(X_te)
labels = list(le.classes_)
rc_open_idx = labels.index('RC_open')
rlc_open_idx = labels.index('RLC_open')
test_indices = list(pd.Series(range(len(df))).sample(frac=0.2, random_state=42).sort_values().index)
test_circuits = df.iloc[test_indices]['circuit'].values
def apply_topology_rule(pred_array):
pred = pred_array.tolist()
for i in range(len(pred)):
if pred[i] == rlc_open_idx and test_circuits[i] == 'RC':
pred[i] = rc_open_idx
return np.array(pred)
print('Training models...')
configs = {
'Linear\n(default)': SVC(kernel='linear', C=1.0, decision_function_shape='ovo', random_state=42),
'RBF\n(default)': SVC(kernel='rbf', C=1.0, gamma='scale', decision_function_shape='ovo', random_state=42),
'Poly\n(default)': SVC(kernel='poly', C=1.0, gamma='scale', degree=3, coef0=1, decision_function_shape='ovo', random_state=42),
'Linear\n(tuned)': SVC(kernel='linear', C=100, decision_function_shape='ovo', random_state=42),
'RBF\n(tuned)': SVC(kernel='rbf', C=100, gamma=0.1, decision_function_shape='ovo', random_state=42),
'Poly\n(tuned)': SVC(kernel='poly', C=100, gamma=0.1, degree=3, coef0=1, decision_function_shape='ovo', random_state=42),
}
accs = {}
for name, clf in configs.items():
clf.fit(X_tr, y_tr)
pred = apply_topology_rule(clf.predict(X_te))
accs[name] = accuracy_score(y_te, pred)*100
print(f' {name.replace(chr(10)," "):<22}: {accs[name]:.2f}%')
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
95

## Slide 98
CODE APPENDIX · STEP 8 OF 9
Generating the Results Dashboard (3/5)
regenerate_dashboard.py (continued)
best_clf = configs['RBF\n(tuned)']
best_pred = apply_topology_rule(best_clf.predict(X_te))
best_acc = accs['RBF\n(tuned)']
cm = confusion_matrix(y_te, best_pred)
lin_clf = configs['Linear\n(tuned)']
importance = np.mean(np.abs(lin_clf.coef_), axis=0)
feat_imp_df = pd.DataFrame({'feature':FEATURE_NAMES,'importance':importance}).sort_values('importance',ascending=True)
y_test_labels = le.inverse_transform(y_te)
y_pred_labels = le.inverse_transform(best_pred)
circuit_accs = {}
for circ in ['RC','RLC','SALLEN_KEY','RC_LADDER']:
mask = np.array([circ+'_' in l for l in y_test_labels])
if mask.sum()>0:
circuit_accs[circ] = np.sum(y_test_labels[mask]==y_pred_labels[mask])/mask.sum()*100
print('\nBuilding final dashboard...')
fig = plt.figure(figsize=(24,20))
fig.patch.set_facecolor('#f8f9fa')
gs = gridspec.GridSpec(3,3,figure=fig,hspace=0.45,wspace=0.35)
TK = dict(fontsize=13,fontweight='bold',pad=10)
C6 = ['#90caf9','#90caf9','#90caf9','#1565c0','#1565c0','#1565c0']
ax1 = fig.add_subplot(gs[0,0])
names=list(accs.keys()); vals=list(accs.values())
bars=ax1.bar(names,vals,color=C6,edgecolor='white',linewidth=0.8,width=0.6)
ax1.axhline(y=best_acc,color='#d32f2f',linestyle='--',linewidth=1.5,label=f'Best {best_acc:.1f}%')
ax1.set_ylim(60,95); ax1.set_ylabel('Test Accuracy (%)',fontsize=10)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
96

## Slide 99
CODE APPENDIX · STEP 8 OF 9
Generating the Results Dashboard (4/5)
regenerate_dashboard.py (continued)
ax1.set_title('Kernel Comparison\nDefault vs Tuned + Topology Rule',**TK) ax1.legend(fontsize=8) for bar,val in zip(bars,vals): ax1.text(bar.get_x()+bar.get_width()/2,bar.get_height()+0.3,f'{val:.1f}%',ha='center',va='bottom',fontsize=8,fontweight='bold') ax1.tick_params(axis='x',labelsize=8); ax1.set_facecolor('#ffffff') ax2 = fig.add_subplot(gs[0,1]) cn=list(circuit_accs.keys()); cv=list(circuit_accs.values()) cc=['#ef9a9a' if v<70 else '#fff176' if v<85 else '#a5d6a7' for v in cv] bars2=ax2.bar(cn,cv,color=cc,edgecolor='grey',linewidth=0.8,width=0.5) ax2.set_ylim(0,115); ax2.set_ylabel('Accuracy (%)',fontsize=10) ax2.set_title('Per-Circuit Accuracy\n(RBF Tuned + Topology Rule)',**TK) for bar,val in zip(bars2,cv): ax2.text(bar.get_x()+bar.get_width()/2,bar.get_height()+1,f'{val:.1f}%',ha='center',va='bottom',fontsize=9,fontweight='bold') ax2.tick_params(axis='x',labelsize=9); ax2.set_facecolor('#ffffff') ax3 = fig.add_subplot(gs[0,2]) fc=df.groupby('fault').size() ax3.pie(fc.values,labels=fc.index,autopct='%1.1f%%', colors=['#ef5350','#42a5f5','#66bb6a','#ffa726','#ab47bc'], startangle=90,textprops={'fontsize':9}) ax3.set_title(f'Dataset Composition\n({len(df)} total samples)',**TK) ax4 = fig.add_subplot(gs[1,0]) bc=['#1565c0' if v>=feat_imp_df['importance'].quantile(0.75) else '#90caf9' for v in feat_imp_df['importance']] ax4.barh(feat_imp_df['feature'],feat_imp_df['importance'],color=bc,edgecolor='white') ax4.set_xlabel('Mean |Coefficient|',fontsize=10) ax4.set_title('Feature Importance\n(Linear SVM Weights)',**TK) ax4.tick_params(axis='y',labelsize=8); ax4.set_facecolor('#ffffff')
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
97

## Slide 100
CODE APPENDIX · STEP 8 OF 9
Generating the Results Dashboard (5/5)
regenerate_dashboard.py (continued)
ax5 = fig.add_subplot(gs[1,1:]) f1s=f1_score(y_te,best_pred,average=None) f1_df=pd.DataFrame({'class':labels,'f1':f1s}).sort_values('f1',ascending=True) f1c=['#d32f2f' if f==0 else '#ef9a9a' if f<0.5 else '#fff176' if f<0.8 else '#a5d6a7' for f in f1_df['f1']] ax5.barh(f1_df['class'],f1_df['f1'],color=f1c,edgecolor='white',height=0.7) ax5.axvline(x=0.5,color='orange',linestyle='--',alpha=0.7,linewidth=1.5) ax5.axvline(x=0.8,color='green',linestyle='--',alpha=0.7,linewidth=1.5) for i,(_,row) in enumerate(f1_df.iterrows()): ax5.text(row['f1']+0.01,i,str(round(row['f1'],2)),va='center',fontsize=8) ax5.set_xlabel('F1 Score',fontsize=10); ax5.set_xlim(0,1.2) ax5.set_title('Per-Class F1 — RBF + Topology Rule (Final)',**TK) ax5.set_facecolor('#ffffff') ax6 = fig.add_subplot(gs[2,:]) sns.heatmap(cm,annot=True,fmt='d',cmap='Blues',xticklabels=labels,yticklabels=labels, linewidths=0.3,ax=ax6,cbar_kws={'shrink':0.8},annot_kws={'size':7}) ax6.set_xlabel('Predicted',fontsize=11); ax6.set_ylabel('Actual',fontsize=11) ax6.set_title('Confusion Matrix — RBF + Topology Rule | Accuracy: ' + str(round(best_acc,2)) + '%',**TK) ax6.tick_params(axis='x',labelsize=7,rotation=45) ax6.tick_params(axis='y',labelsize=7,rotation=0) # CORRECTED TITLE - SN Bose Summer Internship, NIT Silchar (not Research Centre) fig.suptitle('Kernel-Based Fault Classification in Analog Circuits\nSN Bose Summer Internship 2026, NIT Silchar — FINAL Results (78.43%, Topology-Aware)', fontsize=16,fontweight='bold',y=0.98) out_path = os.path.join(OUT_DIR,'results_dashboard_FINAL.png') plt.savefig(out_path,dpi=150,bbox_inches='tight',facecolor=fig.get_facecolor()) plt.close() print('Dashboard saved -> ' + out_path)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
98

## Slide 101
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (1/6)
app.py — The live demo: loads the saved model, applies the topology-aware correction rule, and serves the interactive prediction UI
import streamlit as st
import joblib
import numpy as np
import pandas as pd
import os
st.set_page_config(
page_title="Analog Circuit Fault Classifier",
layout="wide"
)
# ---- Header ----
st.title("Kernel-Based Fault Classification in Analog Circuits")
st.markdown("""
**SVM-based fault classifier** trained on real LTspice parameter sweep simulation data.
Classifies faults across **4 circuit topologies** (RC, RLC, Sallen-Key, RC Ladder)
and **5 fault types** (Normal, Drift, Open, Short, Noise).
**Final accuracy: 78.43%** on 20-class problem (RBF kernel + topology-aware correction)
""")
# ---- Load model artifacts ----
@st.cache_resource
def load_artifacts():
model = joblib.load("model/model.pkl")
scaler = joblib.load("model/scaler.pkl")
le = joblib.load("model/label_encoder.pkl")
return model, scaler, le
model, scaler, le = load_artifacts()
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
99

## Slide 102
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (2/6)
app.py (continued)
# ---- Tabs ----
tab1, tab2, tab3 = st.tabs(["Dashboard", "Try Prediction", "Dataset"])
# ===== TAB 1: Dashboard =====
with tab1:
st.header("Results Dashboard")
if os.path.exists("results/results_dashboard_FINAL.png"):
st.image("results/results_dashboard_FINAL.png", use_column_width=True)
else:
st.warning("Dashboard image not found")
st.header("Final Results Summary")
col1, col2, col3 = st.columns(3)
col1.metric("Overall Accuracy", "78.43%")
col2.metric("RLC Accuracy", "100%")
col3.metric("RC_open F1 (recovered)", "0.462")
st.markdown("""
| Kernel | Default | Tuned + Topology Rule |
|--------|---------|------------------------|
| Linear | 77.94% | 77.45% |
| RBF | 71.08% | **78.43%** |
| Polynomial | 75.49% | 77.94% |
""")
# ===== TAB 2: Try Prediction =====
with tab2:
st.header("Try a Prediction")
st.write("""
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
100

## Slide 103
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (3/6)
app.py (continued)
Select a sample from the dataset or enter feature values manually
to see the model's fault classification.
""")
df = pd.read_csv("data/features_v2.csv")
df["label"] = df["circuit"] + "_" + df["fault"]
feature_cols = [f"f{i}" for i in range(1, 18)]
feature_names = [
"peak_voltage","rms_value","mean_voltage","std_voltage",
"rise_time","settling_time","skewness","kurtosis",
"dominant_freq","spectral_energy","spec_centroid",
"bandwidth","spec_entropy","energy",
"zero_crossing_rate","crest_factor","dc_level"
]
mode = st.radio("Input method:", ["Pick a sample from dataset", "Enter values manually"])
if mode == "Pick a sample from dataset":
sample_idx = st.selectbox(
"Choose a sample (shown as circuit_fault, true label):",
options=df.index,
format_func=lambda i: f"#{i} — {df.loc[i,'label']}"
)
row = df.loc[sample_idx]
true_label = row["label"]
X_input = row[feature_cols].values.reshape(1, -1)
circuit_input = row["circuit"]
st.write(f"**True label:** {true_label}")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
101

## Slide 104
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (4/6)
app.py (continued)
else: st.write("Enter the 17 feature values:") cols = st.columns(3) values = [] for i, fname in enumerate(feature_names): with cols[i % 3]: val = st.number_input(f"{fname} (f{i+1})", value=0.0, format="%.4f") values.append(val) X_input = np.array(values).reshape(1, -1) circuit_input = st.selectbox("Circuit type (for topology rule):", ["RC", "RLC", "SALLEN_KEY", "RC_LADDER"]) true_label = None if st.button("Predict Fault Type", type="primary"): X_scaled = scaler.transform(X_input) pred = model.predict(X_scaled)[0] pred_label = le.inverse_transform([pred])[0] # Apply topology-aware rule labels_list = list(le.classes_) rlc_open_idx = labels_list.index("RLC_open") rc_open_idx = labels_list.index("RC_open") if pred == rlc_open_idx and circuit_input == "RC": pred = rc_open_idx pred_label = "RC_open" st.info("Topology-aware correction applied: RLC_open → RC_open " "(an RC circuit cannot have an RLC-type fault)")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
102

## Slide 105
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (5/6)
app.py (continued)
st.success(f"**Predicted:** {pred_label}") if true_label is not None: if pred_label == true_label: st.success("Correct prediction!") else: st.error(f"Incorrect — true label was {true_label}") # Show prediction probabilities probs = model.predict_proba(X_scaled)[0] prob_df = pd.DataFrame({ "Class": le.classes_, "Probability": probs }).sort_values("Probability", ascending=False).head(5) st.write("**Top 5 class probabilities:**") st.dataframe(prob_df, hide_index=True) # ===== TAB 3: Dataset ===== with tab3: st.header("Dataset Overview") df = pd.read_csv("data/features_v2.csv") df["label"] = df["circuit"] + "_" + df["fault"] st.write(f"**Total samples:** {len(df)}") st.write(f"**Classes:** {df['label'].nunique()} (4 circuits × 5 fault types)") st.subheader("Samples per class") counts = df.groupby(["circuit", "fault"]).size().reset_index(name="count") st.dataframe(counts, hide_index=True)
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
103

## Slide 106
CODE APPENDIX · STEP 9 OF 9
The Streamlit Web App (6/6)
app.py (continued)
st.subheader("Feature columns (f1-f17)")
feat_table = pd.DataFrame({
"Feature": [f"f{i}" for i in range(1,18)],
"Name": [
"peak_voltage","rms_value","mean_voltage","std_voltage",
"rise_time","settling_time","skewness","kurtosis",
"dominant_freq","spectral_energy","spec_centroid",
"bandwidth","spec_entropy","energy",
"zero_crossing_rate","crest_factor","dc_level"
]
})
st.dataframe(feat_table, hide_index=True)
st.subheader("Raw data sample")
st.dataframe(df.head(10))
# ---- Footer ----
st.markdown("---")
st.markdown("""
**Project:** SN Bose Summer Internship 2026, NIT Silchar | NIT Silchar
**Methodology:** LTspice parameter sweeps → 17-feature extraction → SVM kernel comparison → GridSearchCV tuning → topology-aware post-processing
""")
KERNEL-BASED FAULT CLASSIFICATION IN ANALOG CIRCUITS
104